## Slide 1: Module 6: Cleaning Activities and Checking Your Work
Overview
What is effective cleanup?
Interior cleaning techniques.
Exterior cleaning techniques.
How to check your work.
Cleaning verification procedure.
Clearance testing.
Safe disposal practices.
Notes: What you will learn in this module:
This module will cover all the topics listed on the slide above.
The goal of cleaning is to leave the work area as clean as or cleaner than when you arrived so that, as a result of your work, leaded dust is not left behind to poison the residents.
  At the end of this module, you will know how to check your work to ensure the work area is clean enough to pass the visual inspection and cleaning verification procedure, or pass a clearance examination.
By using the techniques described in this module, you will be able to clean a work area quickly and efficiently. Remember, approaching a cleanup is similar to approaching a job. Proper preparation and planning will help make your cleaning efforts more effective and efficient.
Always schedule time at the end of each day to thoroughly clean the work area.

## Slide 2: What is Effective Cleanup?
Keeping dust from getting back into areas already cleaned.
Using proper cleaning techniques.
Cleaning all surfaces, tools and clothing.
Checking your work.
  Usually will involve performing cleaning verification.
  Could include a clearance examination.
Safe and secure disposal of waste.
Notes: Containment
Effective cleaning begins with proper preparation and containment. Cleaning will be much easier and efficient if proper containment has kept all dust and debris confined to the work area. While cleaning, keeping dust in the area that is being cleaned is also important. You don’t want to have cleaned areas become re-contaminated after cleaning.
Proper cleaning techniques
Follow a “top to bottom, back your way out” approach so that you don’t have to re-enter an area that has already been cleaned. Start cleaning high to low. You should be careful not to spread dust to other areas while cleaning. Follow an ordered sequence of cleaning to ensure that you do not contaminate other areas. For example, if floors are cleaned before the countertops you must walk on the floors to get to the countertops and this risks re-contaminating the floors. Never re-enter areas already cleaned. Also, countertops are higher than floors and can drop dust onto the floors.
Cleaning all surfaces
The term “all surfaces” includes all vertical surfaces such as walls and windows, and all horizontal surfaces such as floors, door tops and moldings, window troughs, and window sills. Cleaning should proceed from high to low, i.e., from top of wall to window to floor.
Checking your work
Conduct a visual inspection after cleaning is completed. Look for paint chips, dust and debris.
Perform cleaning verification until all areas pass when compared to the cleaning verification card.
A dust clearance examination may replace cleaning verification when required by Federal, state, tribal, or local law, or by the owner.
Safe and secure disposal of waste
Bag and “gooseneck seal” all waste in heavy duty plastic bags. Safely dispose of all waste in accordance with Federal, state and local regulations. See slides 6-9 and 6-10 for information on disposal.

## Slide 3: Interior Cleaning Requirements
Collect all paint chips and debris, and seal in heavy duty plastic bags.
Mist, remove, fold (dirty side in) and tape or seal protective sheeting. Dispose of sheeting as waste.
Plastic sheeting between non-contaminated rooms and work areas must remain in place until after cleaning and removal of other sheeting.
HEPA vacuum or wet wipe walls from high to low, then HEPA vacuum remaining surfaces and wipe with a damp cloth.
Clean 2 feet beyond the contained work area.
Use disposable wipes or change cloths frequently.
For carpet or rug, use HEPA vacuum with beater bar.
HEPA vacuum and wet mop uncarpeted floors - two-bucket mopping method or wet mopping system.
Notes: Pick up
Always begin cleaning activities by picking up visible paint chips and debris with a wet disposable cloth without dispersing any of it, and sealing this material in a heavy-duty bag.
When the job is complete, mist the sheeting, fold it (dirty side in), and either seal it with tape, or seal it in a heavy-duty bag. Always fold dirty side inwards, and seal with tape or place in a heavy duty plastic bag. If it is placed in a heavy-duty bag, “gooseneck-seal” the bag and dispose of the bag with the rest of your waste. Dispose of all sheeting as waste by using the correct folding and disposal procedure, after it has been vacuumed.
Clean with a Plan
Start cleaning at the far end of the work area and work back to the exit.
Clean walls with a HEPA vacuum or by wiping with a damp disposable cloth: Start with the tops of the walls, tops of doors and door frames and work down to the floor.
Thoroughly vacuum all remaining surfaces and objects, including furniture and fixtures, in the work area. The HEPA vacuum must be equipped with a beater bar when vacuuming carpeting or rugs.
Wipe all surfaces and objects that remained in the work area, except carpeted or upholstered surfaces, with a damp cloth.
Clean the floor last
Clean with a wet mopping system or a two-sided bucket and mop.
Clean the entire work area and the area within 2 feet of the work area.
If using the two-bucket mopping system, repeat the process using a new mop head and clean water. Remember, always keep one bucket for cleaning solution and the other bucket for wringing out the cloth or mop head. You must keep wash and rinse water separate. Change the rinse water often.
Check your work
Before a Certified Renovator visually inspects the work area, check your work to determine whether dust, debris or residue is still present. If dust, debris or residue is still present, these conditions must be corrected before the visual inspection is performed.

## Slide 4: Visual Inspection Procedure
Conducted by Certified Renovator.
Put on disposable foot covers before entering the work area.
Make sure there is adequate lighting in the work area.
  Turn-on all of the lights or use a bright, white-light flashlight.
Systematically look for dust and debris on every horizontal surface in the work area and 2 feet beyond.
  Work from the farthest area from the entry to the entry.
  Closely examine each surface.
If you find visible dust or debris, then re-clean the work area and repeat step 4.
Once you have carefully looked at all of the surfaces and found no dust or debris, proceed to the cleaning verification procedure or clearance.
Notes: Visual inspection after cleaning is required by the RRP Rule. Visual inspection is just the first step.
A visual inspection must be conducted by a Certified Renovator once cleaning is complete, and prior to the cleaning verification or clearance examination of the work area.
In a visual inspection, the Certified Renovator looks for visible paint chips, dust and debris.
Make sure that adequate lighting is provided during the cleaning and visual inspection of the work area. You cannot see dust and small paint chips without adequate lighting.
Inspect the entire work area and the area 2 feet beyond the work area on all sides of the containment.
Visual inspection of the work area alone will not verify that the work area has been cleaned adequately – visual inspection is only the first step. In many instances, leaded dust is not visible to the naked eye and will not be detected during a visual inspection. Once the visual inspection has been completed and no visible dust and debris are present, the work area must pass either the cleaning verification procedure or a clearance examination in order for the project to be completed in compliance with the RRP Rule.
Whether the cleaning verification procedure or clearance examination is conducted will be based on regulatory requirements or terms in the renovation contract.

## Slide 5: Cleaning Verification (CV) Procedure
Wipe each window sill within the work area. Use a single wet disposable cleaning cloth per window sill.
Wipe uncarpeted floors and all countertops with wet disposable cleaning cloths. Wipe up to a maximum of 40 ft2 per cloth.
Compare each wipe to the CV card. If the cloth matches or is lighter than the CV card, the surface has passed cleaning verification and no further action is required.
If the cloth is darker than the CV card, re-clean and repeat the CV process.
If the second wet cloth fails, wait 1 hour or until surfaces are dry, and then wipe with an electrostatically-charged white disposable cleaning cloth designed to be used for cleaning hard surfaces. This completes the cleaning verification.
Notes: After visual inspection, one of two activities must be conducted. A Certified Renovator must perform cleaning verification or other certified professionals must conduct a clearance examination. The steps for the cleaning verification procedure are explained below.
Window Sills
  Using a single, wet, disposable cleaning cloth, wipe the entire surface of each window sill in the work area.
Wipe Countertops and Floors
  Wipe the entire surface of each countertop and uncarpeted floor within the work area with wet disposable cleaning cloths. Floors must be wiped using a wet cleaning system, including a long handle device with a head to which a wet disposable cleaning cloth is attached. The cloth must remain damp at all times while being used to wipe the floor.
  If the surface of a countertop or floor within the work area is greater than 40 square feet, the surface within the work area must be divided into roughly equal sections that are each less than 40 square feet. Wipe each surface section separately using a new wet disposable cleaning cloth.
Interpret the Cleaning Verification Procedure.
  Compare each wipe representing a specific surface section to the cleaning verification card. If the cloth used to wipe each surface section within the work area matches or is lighter than the cleaning verification card, that surface section has been adequately cleaned.
  If the cloth is darker than the cleaning verification card, re-clean that surface section, then use a new wet disposable cleaning cloth to wipe the surface section. If the cloth matches or is lighter than the cleaning verification card, that surface section has been adequately cleaned.
  If the second cloth does not match and is not lighter than the cleaning verification card, re-clean the surface and wait for 1 hour or until the surface section has dried completely, whichever is longer. Then wipe the surface section with an electrostatically charged white disposable cleaning cloth designed to be used for cleaning hard surfaces. The cleaning verification procedure is now complete and the surface is considered clean.
  When cleaning verification has been completed for all of the surfaces in the work area (including window sills), warning signs may be removed.

## Slide 6: Dust Clearance Examination
A dust clearance examination may be performed instead of cleaning verification.
  A clearance examination must be a conducted by a Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician.
  If clearance fails, the renovation firm must re-clean the work area until dust standards comply with applicable state, territorial, tribal and local standards.
Notes: Clearance Examination (Dust Clearance Testing) – Optional under the RRP Rule
Dust clearance testing may be performed to check the effectiveness of the cleaning efforts. Clearance is an option under the EPA Renovation, Repair, and Painting Rule and is required by the HUD Rule in many cases.
Dust clearance testing is performed to check the effectiveness of cleaning efforts.
In some cases, dust clearance testing may be required as part of “clearance” (a regulation-defined process to ensure that a work area is not contaminated with leaded dust after work is completed). Cleaning verification need not be performed if dust clearance testing is required at the conclusion of a renovation. In such cases, dust clearance testing may only be performed by a Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician. The Certified Renovation Firm is required to re-clean the work area until dust-lead levels in the work area meet the clearance standards. Some state, local, and tribal laws may require a clearance examination following renovation and remodeling work, to levels that differ from the Federal clearance standards. The selection of a CV or a clearance examination will be based on regulatory requirements or the renovation contract.
    Clearance is required in many pre-1978 properties receiving Federal housing assistance. The clearance examination may be scheduled by the agency administering the assistance. A clearance examination is performed by a trained person independent of the renovation firm performing the work. Ask your client or contact the agency administering the assistance to the property to find out if a clearance examination is required at the end of the job and to find out who will schedule it. Remember, if the property fails clearance, the unit must be re-cleaned and another clearance examination performed. Sometimes the cost of re-cleaning and the additional clearance examination will be the responsibility of the contractor. Cleaning well the first time will saves both time and money.

## Slide 7: Exterior Cleanup Requirements
Clean all surfaces in the work area until no visible dust, debris, or residue remains.
Remove all dust and debris without dispersal, and seal in heavy plastic bags.
Remove protective plastic sheeting and mist before folding it dirty side inward.
Check your work.
  Focus on areas such as window sills, bare soil, and children’s play areas.
  Look for dust, debris and paint chips.
Notes: Specific exterior jobs
If work takes place on an exterior porch or stairwell, HEPA vacuuming, wet cleaning and mopping, in addition to a thorough visual inspection, should be used to clean the work area. For such jobs, the cleanup can be similar to cleanup after interior jobs. Collect and dispose of any dust and debris with the rest of your waste.
Remember
Lead contaminated soil can poison children.
Avoid dry raking and shoveling, and spreading dust. However, raking and shoveling the soil is appropriate if it is misted first.
Protective sheeting
Collect all dust and debris on the sheeting and place in plastic bags.
Mist sheeting, fold dirty side inward, and dispose of as waste. This is especially important since you will not be cleaning the ground afterward. Remember that you are responsible to make sure you do not leave dust and debris behind.
The Certified Renovator should visually inspect the plastic after cleaning for dust and debris. Remember the Certified Renovator is required to certify that the work area was cleaned properly at the end of the job.
Protective sheeting is to be disposed of as waste.
Visual inspection
A thorough visual inspection of the work area should be conducted after any exterior job. Any visible paint chips, wood chips and other debris from the work area should be collected and disposed of with the rest of your waste.
Focus your visual inspection on areas such as exterior porches, outside play areas, bare soil and ground, and window sills, but don’t ignore or neglect other areas.

## Slide 8: Exterior – Check Effectiveness of Cleaning
Visual inspection
  A Certified Renovator conducts a visual inspection after any cleaning.
  Determines if any visible dust and debris are present in and beyond the boundaries of the work area.
If visible dust or debris are found, collect and dispose of all paint chips, dust, and debris identified during the visual inspection.
After re-cleaning, the Certified Renovator conducts another visual inspection.
When all areas pass, warning signs may be removed.
Notes: Checking your work
A thorough visual inspection is the main part of checking your cleanup after an exterior job. You should collect and dispose of any paint chips, wood chips and debris found during the visual inspection.
A visual inspection is conducted after completing cleanup, to check your work.
The Certified Renovator must perform the visual inspection to determine whether dust, debris or residue is still present on surfaces in or below the work area, including window sills and on the ground.
If dust or residue is present, clean again, and then repeat the visual inspection.
Warning signs may be removed after passing visual inspection.
    Clearance on exterior jobs. For exterior jobs, HUD requires only a visual assessment of the work area to pass clearance. No dust or soil testing is required. If you follow procedures taught in this course you will satisfy HUD requirements.

## Slide 9: Disposal
What should I do with my waste?
At the work site:
  Place waste in heavy duty plastic bag.
  “Gooseneck seal” the bag with duct tape.
  Carefully dispose of waste in accordance with Federal and other regulations.
  HEPA vacuum the exterior of the waste bag before removing it from the work area.
  Store waste in a secure area.
Notes: At the Work Site
Always collect, bag and seal all waste at the work site and in the work area. HEPA vacuum or wipe the exterior of waste bags before removing them from the work area. Do not carry your waste to another room or another area before bagging and sealing it. Store all waste in a secure container or dumpster until disposal. Limit on-site storage time. Avoid transporting waste in an open truck or in a personal vehicle. Some examples of waste include protective sheeting, HEPA filters, paint chips, dust, dirty water, used cloths, used wipes, used mop heads, used protective clothing, used respirators, used gloves, and architectural components. Architectural components that are too big to fit into bags must be wrapped in plastic and sealed with tape prior to removal from the work area. If needed, “double-bag” your waste to help prevent the waste from escaping if the bag is cut or ripped.
Waste Water
Water used for cleanup should be filtered and dumped in a toilet if local rules allow. Never dump this water down a sink or tub, down a storm drain or on the ground. Filtering waste water through a 5-micron filter may be necessary when lead-contamination such as paint chips and dust may be present in the water. Check with your local water treatment authority, and in Federal and state regulations for more information.
Always dispose of waste water in accordance with Federal, state and local regulations.
    HUD recommends that when building components are recycled or sold, painted building components should be stripped before re-installation. If components are not stripped, they should never be reinstalled in housing.

## Slide 10: Disposal – Federal, State and Local Information
According to Federal law:
  In housing: Waste must be disposed of as normal household waste.
  In non-residential child-occupied facilities: If waste exceeds 220 lbs, treat all debris as hazardous.
Always check local requirements!
Notes: Waste Disposal Issues
Because EPA considers most residential renovation and remodeling as “routine residential maintenance”, the waste generated during these activities is classified as solid, non-hazardous waste, and should be taken to a licensed solid waste landfill. This does not apply to commercial, public or other non-residential child-occupied facilities.
  If you generate any hazardous waste, you should determine whether you generate more than 220 pounds of hazardous waste per job site per month. If you have less than 220 pounds per location per month, manage the waste as solid, non-hazardous waste. If you generate more than 220 pounds of hazardous waste, you should contact your state and local regulators to find out how to properly dispose of it.
  Some possible examples of hazardous waste include: paint chips; vacuum debris; sludge or chemical waste from strippers; and, HEPA filters.
  Some possible examples of non-hazardous waste may include: disposable clothing; respirator filters; rugs and carpets; protective sheeting; and, solid components with no peeling paint.
  All waste should be sealed in heavy duty heavy duty plastic bags and handled carefully.
  Large architectural components should be wrapped and sealed in plastic sheeting, and disposed of along with other waste.
  Always check Federal, state and local requirements before disposing of waste. Some states have enacted more stringent waste management and disposal requirements than Federal regulations. You need to become aware of how Federal, state and local requirements affect the management and disposal of renovation waste in your area.

## Slide 11
Exercise: Cleaning and the Cleaning Verification Procedure
Work in groups of 2-6.
Assignments:
  Skill Set #7: Interior Final Cleaning
  Skill Set #8: Exterior Final Cleaning
  Skill Set #9: Bagging Waste
  Skill Set #10: Visual Inspection
  Skill Set #11: Cleaning Verification Procedure
Choose the tools and supplies you need to clean the work area.
Clean your work area.
You have 40 minutes.
Notes: Exercise: Cleanup and Cleaning Verification
This exercise gives you a chance to demonstrate cleanup, visual clearance, cleaning verification, and proper waste-bagging techniques. The slide provides basic
instruction.
  Stay in your groups of 2 to 6 students, in your work area.
  Choose the right tools. Tools available include buckets, mops, water, detergent, HEPA vacuum, wipes, plastic sheeting, plastic bags, tape, etc.
  Clean up the dust.
  Bag the waste.
  Check your work.
  Verify cleaning.

## Slide 12: Now You Know…
How to clean the work area systematically.
How to check the effectiveness of cleaning.
How to perform a visual inspection of the work area.
How to perform the cleaning verification procedure.
How to release the work area for clearance testing.
How to properly dispose of waste.
Notes: The information on the slide above summarizes the topics covered in this module.