## Slide 1: Module 3: Before Beginning Work
Overview
This module teaches you:
To educate owners and residents.
That the use of lead-based paint was widespread.
To determine if lead-based paint is present.
To use EPA-recognized test kits to check for lead-based paint.
How to decide which rule(s) apply.
Notes: Module Overview
The module also considers the important questions that must be asked at the beginning of a job to establish whether a job is covered by the RRP Rule and/or the HUD Rules, and what requirements apply.

## Slide 2
Educate Owners and Residents
The Pre-Renovation Education Rule:
  Requires Renovation Firms to provide the Renovate Right pamphlet to owners/residents prior to renovation activities in pre-1978 housing and child-occupied facilities.
  Specifies requirements for educating residents/occupants and delivering the Renovate Right pamphlet that vary by type of property and the area being renovated.
Under the RRP Rule, Certified Firms MUST:
  Give homeowners/residents and child-occupied facility owners/adult representatives copies of the Renovate Right pamphlet.
  Let parents/guardians of children using a child-occupied facility know about the renovation and how to get a copy of the Renovate Right pamphlet.
  Get confirmation of receipt of the Renovate Right pamphlet from owners, or evidence that the pamphlet was delivered to tenants/residents.
  Keep all records for at least 3 years.
Notes: 3-<number>
<header>
<date/time>
Exclusions: The Pre-Renovation Education Rule covers the same renovation activities that are covered by the Renovation, Repair, and Painting Rule. The same exclusions apply, except that the owner/occupant cannot opt out of pamphlet delivery. (Refer to Module 2 for more information on exclusions.)
Work in Homes: No more than 60 days before beginning a renovation, Certified Renovation Firms must distribute the Renovate Right pamphlet to the owners and residents of the pre-1978 housing to be renovated.
  Firms must either obtain the owner’s written acknowledgment or proof that the pamphlet was sent by certified mail, return receipt requested, at least 7 days before the renovation began.
  For tenants, Certified Firms must either obtain a written acknowledgment of receipt, or document that the firm delivered the pamphlet and was unable to obtain a written acknowledgment.
  All proof of receipt/mailing/delivery records must be kept for 3 years after completion of the renovation.
  Sample forms to document confirmation of receipt are included in the Renovate Right pamphlet.
Work in Common Areas: No more than 60 days before beginning a renovation, Certified Renovation Firms must provide the Renovate Right pamphlet to the owner of pre-1978 housing being renovated. Firms must provide written notification to all residents in the affected units of the property being renovated, must notify affected residents about where information is posted if work in nearby common areas will affect them. The following information should be posted about work in common areas:
  Describing the nature and location of the work;
  Listing the work start and end dates; and,
  Providing the Renovate Right pamphlet or information on how to obtain a free copy of the pamphlet.
This information may be provided to tenants by mail, hand-delivery, or by posting signs containing this information where they are likely to be seen by the residents of all affected units.
Work in Child-Occupied Facilities: No more than 60 days before beginning a renovation, Certified Renovation Firms must distribute the Renovate Right pamphlet to the owner of the building and to an adult representative of the child-occupied facility, following the same documentation requirements as for homes. Firms must also provide notification to parents and guardians of children using the child-occupied facility, following the same requirements as for tenants affected by renovations in common areas.
To obtain copies of the Renovate Right pamphlet visit the EPA website at www.epa.gov/lead, or contact the National Lead Information Center at 1-800-424-LEAD (5323). The pamphlet may be copied for distribution as needed to comply with pre-renovation education requirements.

## Slide 3: How Widespread is Lead-Based Paint in Housing?
Notes: Source of data in table above: American Healthy Homes Survey: Draft Final Report for Peer Review: Lead and Arsenic Findings, October 7, 2008.
Homes built in 1978 and earlier
Approximately 34 million pre-1978 housing units contain paint that meets the Federal definition of “lead-based paint” (Source: American Healthy Homes Survey: Draft Final Report for Peer Review: Lead and Arsenic Findings, October 7, 2008).
  EPA’s RRP Rule assumes that any house built before 1978 contains lead-based paint, unless the house has been tested for lead-based paint and the results indicate that the house does not contain lead-based paint.
  Components most likely to be coated with lead-based paint include windows and doors (interior and exterior), as well as exterior walls and porches.
Homes built before 1960
Homes built before 1960 are more likely than homes built after 1960 to contain lead-based paint and are also more likely to have deteriorated paint surfaces due to age. In addition, concentrations of lead in paint were higher prior to the 1950’s when paint companies began to use less lead in paint they manufactured.
Consider:
  86% of pre-1940 homes contain lead-based paint on at least one surface.
  66% of homes built from 1940 to 1959 contain lead-based paint on at least one surface.
Note: Determining the age of the property may require some investigation. If the owner does not know or have access to records, property information in many localities can be accessed from review of court registration or tax records held by the office of the tax assessor in the community or county where the property is located. If you don’t know the age of the building, assume it was built before 1978.

## Slide 4: How to Determine if Lead-Based Paint is Present
Paint testing must be performed prior to renovation on all surfaces to be affected by the work, or you must presume the paint is lead-based. Any testing must be performed by the appropriate qualified professional.
Type of Paint Testing for Renovations | Who can do the testing?
EPA-recognized test kits | Certified Renovators
X-Ray Fluorescence instruments (surface-by-surface) | Certified lead-based paint inspectors or risk assessors
Paint chip sampling and laboratory testing | Certified lead-based paint inspectors or risk assessors
Notes: Surface-by-Surface or Limited Testing: Lead-based paint can only be identified by testing paint. A surface-by-surface evaluation of painted surfaces (a lead inspection) and all paint-chip sampling must be conducted by a Certified Lead Inspector or Certified Lead Risk Assessor. Whether paint testing is accomplished by an inspection or by limited testing, the results of testing only apply to the work if the surfaces covered by the renovation are covered by the testing report. A property owner may provide a report from a Certified Lead Inspector/Risk Assessor that proves no lead-based paint is present, in lieu of testing affected surfaces. If no testing result is available, test the paint or presume lead-based paint is present.
EPA-Recognized Test Kits: Check the EPA website at www.epa.gov/lead for information on EPA-recognized test kits and how to use them. EPA is currently reviewing more sensitive test kits which may come on the market. All test kits currently on the market are colorimetric tests for lead; that is, they change color when lead is present. Different test kit chemicals produce different colors when lead is present. All paint layers must be tested when using test kits. Make sure to follow the manufacturer’s instructions when using this testing method. If there is no color change on the paint film tested, lead-based paint is not present and lead-safe work practices are not required on that surface. Test kit sampling is intrusive and damages each surface tested. Common kit types include:
  Rhodizonate-based test kits that produce a pink to red color when lead is present. This test cannot be used on paint colors such as reds, oranges and pinks which make seeing any color change difficult. Rhodizonate test kits should not be used to test paint on drywall and plaster surfaces; and,
  Sulfide-based test kits that produce a dark grey to black color when lead is present. Dark colored paints, like dark greens blues and, especially, black make seeing any color change difficult. Sulfide test kits should not be used to test paint on metal surfaces.
X-Ray Fluorescence Testing: Requires a special instrument and a specially-trained Certified Lead Inspector or Certified Lead Risk Assessor. The instrument tests by bombarding the paint film with gamma radiation that causes the lead in the paint to emit x-rays that can be read by a sensor in the instrument. The amount of lead in the paint is directly related to the x-rays read by the sensor. A computer program in the instrument calculates how much lead is in the paint film. This testing method is non-intrusive and is the most used.
Paint-Chip Collection for Laboratory Analysis: Paint-chip testing requires intrusive sampling. All paint layers are removed from the surface being tested. The resulting sample is sent to an EPA-recognized laboratory where it is analyzed to determine how much lead is present. Paint chips may only be collected by Certified Lead Inspectors or Certified Lead Risk Assessors. Laboratory charges are based on turnaround time, and it usually requires a day or two to get results. Intrusive sampling makes repair of tested surfaces necessary.

## Slide 5: Using EPA-Recognized Test Kits to Check for Lead-Based Paint
EPA-recognized test kits:
  Until 9/01/10, EPA will only require the use of test kits that verify the absence of lead-based paint.
  After 9/01/10, test kits must be able to determine whether or not lead-based paint is present.
Submit a testing report of results from use of an EPA-recognized test kit to the client as soon as possible, but no later than 30 days after completing the renovation.
Notes: If test kits are used, you must use an EPA-recognized test kit.
  Until September 1, 2010, EPA is only requiring the use of test kits that determine that lead-based paint is not present on the surfaces tested. If a color change does not occur, lead-safe work practices are not required. If a color change occurs, the change does not with certainty mean that lead-based paint is present. However, the surface must still be presumed to be coated with lead-based paint.
  To be EPA-recognized after September 1, 2010, a test kit must be able to identify lead-based paint. At that time, a test kit positive test result will mean that lead-based paint is present in the coating and that lead-safe work practices must be followed when that surface is disturbed. A negative test result will mean that lead safe-work practices are not required.
  If the test kit gives a positive result on any of the tested surfaces, lead-safe work practices must be used. Alternatively, sampling may be performed by a Certified Lead Inspector or Risk Assessor to determine whether or not lead-based paint is present.
  If test kits are used, Certified Renovators must use an EPA-recognized test kit in order to test affected surfaces. EPA-recognized test kits will be listed on the EPA website at www.epa.gov/lead.
What should be tested?
  Each building component to be renovated or disturbed by renovation must be tested, unless the component is a part of a larger component system and is representative of the whole system. In this case, a single component may represent the larger system. For instance, a stair tread may represent the whole stair system if the painting history of both is similar. If the painting histories are similar and the tested tread shows a negative test for lead-based paint, then the RRP Rule does not apply to the stair system.
Reporting
  When EPA-recognized test kits are used, the Certified Firm must provide a report to the client within 30 days after completion of the renovation. The date of testing, identification of and contact information for the Certified Firm and Certified Renovator performing the testing, test kit manufacturer’s name and kit identification, locations of surfaces tested, descriptions of the surfaces tested, and the results of testing must be included in the report to the owner.

## Slide 6: Test Kit Hands-on
Purpose: The purpose of this hands-on exercise is to teach Certified Renovators how to correctly use EPA-recognized test kits to determine if lead-based paint is present on components and surfaces affected by renovation work.

## Slide 7: Using Decision Logic Charts
Using the following pages, you will practice use of the decision logic charts found in the Small Entity Compliance Guide to Renovate Right.
The decision logic charts will assist you in making decisions regarding how the EPA RRP Rule applies to your work.
Determine if the property is Federally-assisted and if it is, then determine what to do next.
Notes: The information presented in the Small Entity Compliance Guide to Renovate Right flow charts is intended to assist you in understanding what RRP Rule requirements apply to the renovation you are about to perform and whether the HUD Rule also applies to the project. You will find the Small Entity Compliance Guide to Renovate Right flow charts on the following pages in this module. For a complete copy of the Small Entity Compliance Guide to Renovate Right see Appendix 4.
The Small Entity Compliance Guide to Renovate Right flow charts walk you step-by-step through a decision tree which asks you a series of ordered yes-or-no questions. To use the flow charts, begin at the top of flow chart 1, ask yourself each question. Following the yes-or-no answer arrows to the next appropriate question box. At some point you will come to an arrow with directions about continuing to another flow chart. Follow the direction to whichever flow chart the pathway takes you to, skipping flow charts that do not apply. Whenever a text box gives direction about what to do, write it down to develop a list of actions that must be taken for RRP Rule compliance.
Appendix 2 provides a summary of HUD requirements that apply to work done in homes that receive Federal assistance. Information found in Appendix 2 provides assistance in determining whether the property receives Federal housing assistance and what requirements apply if it does. If the property is pre-1978 and does receive Federal housing assistance, both the HUD Lead Safe Housing Rule and the EPA RRP Rule apply to your renovation work.

## Slide 8: Now You Know…
To properly plan a renovation, you must:
Educate owners and residents.
Determine if lead-based paint is present.
Determine what requirements from the EPA and HUD Rules apply to your renovation activities.