## Slide 1: Module 7: Recordkeeping
Overview:
In this section, you will learn about records required for each job.
Records must be retained and made available to EPA, upon request, for 3 years following completion of renovation.
Notes: Language of the RRP Rule is:
“Firms performing renovations must retain and, if requested, make available to EPA, all records necessary to demonstrate compliance…for a period of three years following completion of the renovation.”
    HUD also has a 3-year record retention requirement for notices, evaluations, and clearance or abatement reports (24 CFR 35.175).

## Slide 2: On-The-Job Records
Copies of Certified Firm and Certified Renovator certifications (must be kept on site).
Lead-based paint testing results when an EPA-recognized test kit is used.
Proof of owner/occupant pre-renovation education.
Opt out certification by owner/occupant, when they qualify to and decide to opt out of the lead-safe work practice requirements.
Non-certified worker training documentation (must be kept on site).
Notes: The Certified Firm must designate (in writing) a Certified Renovator to be responsible for each renovation job in target housing or a child-occupied facility. This is the logical person to organize and maintain on-the-job records during the work. On the jobsite, the records should be kept in a safe, secure, clean and dry place. Once the project is complete, some records can be filed with other firm records while others may need to be moved to the next job site.
Records to be maintained on site include:
  Copy of Certified Firm and Certified Renovator(s) certifications.
  Non-certified worker training documentation.
Records to be maintained to document the job:
  Copy of Certified Firm and Certified Renovator(s) certifications.
  Non-certified worker training documentation.
  Designation of a Certified Renovator to the job.
  Information on and results of use of EPA-recognized test kits provided by a Certified Renovator who acted as the representative of the Certified Firm at the job site and who conducted testing for the presence of lead-based paint on surfaces to be affected by the renovation.
  Lead-based paint inspection reports provided by a Certified Lead Inspector or Certified Lead Risk Assessor, if applicable.
  Proof of owner/occupant pre-renovation education
  Opt-out certification by owner-occupant, when they qualify to, and decide to, opt-out of lead safe work practice requirements.
  Any other signed and dated documents from the owner(s) and/or residents regarding conduct of the renovation and requirements in the EPA RRP Rule.
  All reports required from the Certified Firm and the Certified Renovator by the EPA RRP Rule.

## Slide 3: Recordkeeping: Pre-Renovation Education Records
In Target Housing – Individual units:
  Must acquire either written proof of receipt by an adult occupant or proof of delivery/unsuccessful delivery of Renovate Right, or:
  Written proof of receipt of Renovate Right by owner or proof of mailing (if mailing, send 7 days prior to renovation).
In Target Housing - Common Areas (Two Options):
  Provide written notification to each affected unit and make Renovate Right pamphlet available on request; or:
  Keep copies or pictures of the signs and notices posted.
In Child-Occupied Facilities
  Written proof of receipt of Renovate Right by owner or proof of mailing required (If mailing, send 7 days prior to renovation).
  Maintain proof of receipt by owner or adult representative, or certify in writing that the Renovate Right pamphlet has been delivered to facility.
  Keep copies or pictures of the signs and notices posted.
Notes: In addition to the requirements above, maintain all records for pre-renovation education activities that contain information about the following:
In Target Housing – Individual Units:
  When contacts with the owner and occupants were attempted.
  Written proof of when contacts were made.
In Target Housing – Common Areas:
  Documentation of when and to whom written notification was delivered for each unit affected.
  What notices were posted, and when and where they were posted.
In Child-Occupied Facilities:
  When contacts with the owner and occupants were attempted.
  Written proof of when contacts were made.
  Whether and when contact was made with the owner or adult representative of the child-occupied facility.
  What notices were posted, and when and where they were posted.

## Slide 4: Sample Confirmation of Receipt of Renovate Right
  I have received a copy of the pamphlet, Renovate Right: Important Lead Hazard Information for Families, Child Care Providers and Schools.
  Recipient Signature:__________ Printed Name: __________ Date:__/__/__
Self-Certification Option (for tenant-occupied dwellings only) - If the lead pamphlet was delivered but a tenant signature was not obtainable, you may check the appropriate box below.
  Refusal to sign.
  Unavailable for signature.
Gather the following information:
  Printed name and signature of person certifying lead pamphlet delivery.
  Date and time of lead pamphlet delivery.
  Unit address.

## Slide 5: Recordkeeping: Non-Certified Worker Training
Worker’s name.
Description of lead safe work practices the worker is trained to perform.
Completed and signed skills evaluation checklists.
Date(s) of training.
Name and signature of the Certified Renovator who conducted the training.
Notes: Documentation of Non-Certified Renovation Worker Training
The Certified Renovator who conducted the non-certified worker training must document the information taught to, and skill set proficiencies achieved by, each individual trainee. This training can be conducted in a classroom setting with simulated hands-on or on the job. Documentation may vary for each trainee as not all trainees may be assigned to conduct all lead-safe work practices and the training is only required to be task specific.
To simplify this documentation, your training manual includes a form that can be adapted for documenting hands-on and topical training for non-certified workers (See Appendix 6).

## Slide 6: Recordkeeping: Test Kit Reporting
If an EPA-recognized test kit is used to test surfaces in the work area, the firm must:
  Submit a report to the person contracting for the work within 30 days after the end of the renovation, containing:
    Manufacturer and model of the EPA-recognized test kit.
    A description of of the components tested.
    The location of components tested.
    Results of the testing.
  Retain a copy of the test kit documentation form.
Notes: Checking for Lead-Based Paint With EPA-Recognized Test Kits:
  Check www.epa.gov for a list of EPA-recognized test kits.
  Each component to be renovated or impacted by renovation must be tested. If all surfaces are found to be free of lead-based paint, the RRP Rule does not apply.
  If a set of affected components make up an integrated whole (such as a stair tread or riser within a single staircase; or, a window casing, apron, stool, header or trough in a window case system), then only one of the individual components from that set needs to be tested.
EPA-Recognized Test Kits:
  Until September 1, 2010, EPA is only requiring the use of test kits that determine that lead-based paint is not present on the surfaces tested. If a color change does not occur, lead-safe work practices are not required. If a color change occurs, while the change does not with certainty mean that lead-based paint is present, the surface must be presumed to be coated with lead-based paint.
  To be EPA-recognized after September 1, 2010, a test kit must be able to identify lead-based paint. At that time, a test kit positive test result will mean that lead-based paint is present in the coating and that lead-safe work practices must be followed when that surface is disturbed. A negative test result will mean that lead safe-work practices are not required. These kits may be available as early as September 2009.
  If the test kit positive indicator is present on any of the tested surfaces, lead-safe work practices must be used. Alternatively, sampling may be performed by a Certified Lead Inspector or Risk Assessor to prove by laboratory analysis that lead-based paint is not present.
  Certified Renovators must use an EPA-recognized test kit to test affected surfaces. EPA-recognized test kits are listed on the EPA website at www.epa.gov.
Reporting:
  When test kits are used, within 30 days of completing the renovation, the Certified Renovation firm must provide information on test kit manufacturers and models used for testing, a description of components tested including locations, and the results of testing, to the client who contracted for the renovation.
  Retain a copy of the test kit documentation form.

## Slide 7: Recordkeeping: Post-Renovation Reporting
At the end of each renovation, the Certified Renovator must sign a report including the following information:
  Name of Certified Renovator assigned to lead the project;
  Copy of Certified Renovator certification(s);
  Certification from a Certified Renovator of non-certified worker training, and a list of the topics covered;
  Certification of posting of warning signs;
  Description of chemical spot testing, if any performed;
  Certification by the Certified Renovator of work area containment, on-site waste containment and transport, proper post renovation work area cleaning, and of successful cleaning verification.
  Clearance report, if performed.
Notes: Post-Renovation Reporting
The end of renovation report should describe the whole project from posting signs to cleaning verification or clearance. The report should name the Certified Renovator designated by the Certified Firm as responsible for lead-safe work practices on that project. Also include proof of certification for the designated Certified Renovator. The report also must have a signed statement from the Certified Renovator that covers the following areas:
  Proof of non-certified worker training;
  Proof of posting warning signs;
  Description of results from used of EPA-recognized chemical spot test kits;
  Description of work area containment;
  Description of on-site waste containment and transport;
  Proof of proper post-renovation work area cleaning;
  Records of inspections and/or risk assessments conducted by Certified Lead Inspectors or Risk Assessors, if applicable.
  Proof of successful cleaning verification.
  If dust clearance sampling is performed in lieu of cleaning verification, provide a copy of the dust sampling report to the person who contracted for the renovation within 30 days of the completion of the renovation (see 40 CFR 745.86(d)).

## Slide 8: Now You Know…
To have records available at the work site of:
  Training of Certified Renovators and non-certified renovation workers.
  Certifications for the Certified Firm and Certified Renovators.
To retain all records for at least 3 years after completion of the renovation.
To keep records of:
  Training and certifications for all renovation personnel, and for certification of the firm.
  Distribution of required information.
  Communications with and certifications from owners and residents.
  Work activities in compliance to the Rule.
  Post-renovation reports.